238P Operating Systems, Fall 2018
xv6 Boot Recap:
Transitioning from 16 bit mode to 32 bit mode
3 November 2018
Aftab Hussain
University of California, Irvine

---
BIOS	xv6 Boot loader
what it does
Sets up the hardware.
Transfers control to the Boot Loader.

---
BIOS	xv6 Boot loader
what it does
Sets up the hardware.
Transfers control to the Boot Loader.
how it transfers control to the Boot Loader
Boot loader is loaded from the 1st 512-byte sector of the boot disk.
This 512-byte sector is known as the boot sector.
Boot loader is loaded at 0x7c00.
Sets processor’s ip register to 0x7c00.

---
BIOS	xv6 Boot loader
2 source source files
bootasm.S - 16 and 32 bit assembly code.
bootmain.c - C code.

---
BIOS	xv6 Boot loader
2 source source files
bootasm.S - 16 and 32 bit assembly code.
bootmain.c - C code.
executing bootasm.S
Disable interrupts using cli instruction. (Code).
> Done in case BIOS has setup any of its interrupt handlers were initialized
   while setting up the hardware. Also, BIOS is not running anymore, so better
   to disable them.
> Clear segment registers. Use xor for %ax, and copy it to the rest (Code).
 2.	Switch from real mode to protected mode. (References: a, b).
> Note the difference between processor modes and kernel privilege modes
> We do the above switch to increase the size of the memory we can
  address.

---
BIOS	xv6 Boot loader
2 source source file
executing bootasm.S
m.
 2.	Switch from real mode to protected mode.
Let’s expand on this a little bit

---
Addressing in Real Mode

---
In real mode, the processor sends 20-bit addresses to the memory.
(e.g. Intel processors 8086, 8088).
However, it has eight general 16-bit registers + 16 bit segment registers.
How to generate a 20 bit address from a 16 bit register?

---
Say processor fetches a data read/write instruction.
The processor would then use the data segment register (%ds).
To pass the 16-bit address obtained from %ds
to the memory (which accepts 20-bit addresses) we left
shift the 16-bit register by 4 bits.
This is equivalent to adding the register
to itself 16 times.
(try it out in a bit calculator - e.g. gnu calculator)

---
Say processor fetches a data read/write instruction.
The processor would then use the data segment register (%ds).
To pass the 16-bit address obtained from %ds
to the memory (which accepts 20-bit addresses) we left
shift the 16-bit register by 4 bits.
This is equivalent to adding the register
to itself 16 times.
(try it out in a bit calculator - e.g. gnu calculator)
Use other kinds of
segment registers
for other kinds of instructions.
For example for stack reads/ writes use %ss.

---
So let’s look at how the
address translation process takes place in real mode...

---
16 bits
segment selector
16 bits
offset
CPU

---
32 bits
16 bits
segment selector
16 bits
offset
CPU
logical address
(also known as a
32-bit segment:offset pair)

---
32 bits
16 bits
segment selector
16 bits
offset
xv6 refers to this x86 logical address as a virtual address
CPU
logical address
(also known as a
32-bit segment:offset pair)

---
32 bits
Segment translation hardware
16 bits
segment selector
16 bits
16 bits
offset
segment selector
CPU
logical address
(also known as a
32-bit segment:offset pair)
16 bits
offset

---
32 bits
Segment translation hardware
16 bits
segment selector
16 bits
16 bits
offset
segment selector
left shift by 4
CPU
20 bits
segment selector
logical address
(also known as a
32-bit segment:offset pair)
16 bits
offset

---
20 bits
linear address
32 bits
Segment translation hardware
16 bits
segment selector
16 bits
16 bits
offset
segment selector
left shift by 4
CPU
20 bits
segment selector
add
logical address
(also known as a
32-bit segment:offset pair)
16 bits
offset

---
20 bits
directly corresponds to the
physical address
linear address
32 bits
Segment translation hardware
16 bits
segment selector
16 bits
16 bits
offset
segment selector
left shift by 4
CPU
20 bits
segment selector
add
logical address
(also known as a
32-bit segment:offset pair)
16 bits
offset

---
20 bits
if paging is enabled, this address would go through a further translation process within the paging hardware to generate a physical address
linear address
32 bits
Segment translation hardware
16 bits
segment selector
16 bits
16 bits
offset
segment selector
left shift by 4
CPU
20 bits
segment selector
add
logical address
(also known as a
32-bit segment:offset pair)
16 bits
offset

---
linear address
Segment translation hardware
logical address
CPU
xv6 configures this hardware such that logical and linear addresses are always the same.

---
It follows (without paging) in xv6,
logical address =
linear address =
physical address
linear address
Segment translation hardware
logical address
CPU
xv6 configures this hardware such that logical and linear addresses are always the same.

---
Why the switch to Protected Mode?

---
with 20 bit addresses the maximum size of addressable
memory is 2^20 bytes which is only 1MB.
In Protected Mode, we can address 32 bit addresses,
which allows us to address a memory of size 4GB.
Paging hardware is also enabled in Protected Mode.

---
BIOS	xv6 Boot loader
2 source source file
executing bootasm.S
m.
 2.	Switch from real mode to protected mode.
> To setup the protected mode, the boot loader sets up the segment
   descriptor table, with three entries. Each entry is
   [a base physical address, max virtual address limit (4GB), permission bits]

---
BIOS	xv6 Boot loader
2 source source file
executing bootasm.S
m.
lgdt gdtdesc
gdtdesc:
 .word (gdtdesc - gdt - 1) # sizeof(gdt) - 1
 .long gdt # address gdt
the macros used are defined here
the gdt table
setting up segment descriptor table

---
BIOS	xv6 Boot loader
2 source source file
executing bootasm.S
m.
lgdt gdtdesc
gdtdesc:
 .word (gdtdesc - gdt - 1) # sizeof(gdt) - 1
 .long gdt # address gdt
Assembly Tip:
All assembler directives begin with a period. (Ref.)
the macros used are defined here
the gdt table
setting up segment descriptor table

---
BIOS	xv6 Boot loader
2 source source file
executing bootasm.S
m.
 2.	Switch from real mode to protected mode.
> Now enable protected mode by setting the 1 bit in control register %cr0.
  (Code).

---
BIOS	xv6 Boot loader
2 source source file
executing bootasm.S
m.
 2.	Switch from real mode to protected mode.
> To fully enable protected mode, we need to load a new value into %cs.
> Since %cs cannot be modified directly we setup %cs here: (Code), which
   results in %cs to refer to the code descriptor entry in gdt.

---
BIOS	xv6 Boot loader
2 source source file
executing bootasm.S
m.
 2.	Switch from real mode to protected mode.
> To fully enable protected mode, we need to load a new value into %cs.
> Since %cs cannot be modified directly we ljmp (code), which
   results in %cs to refer to the code descriptor entry in gdt (a 32 bit code seg.)
Assembly Tip:
Long Jump:
ljmp $0xfebc, $0x12345678
Use 0xfebc for the CS register and 0x12345678 for the EIP register. (Ref.)

---
BIOS	xv6 Boot loader
2 source source file
m.
We have completed transitioning from 16 bit (real) mode to 32 bit (protected) mode

---
BIOS	xv6 Boot loader
2 source source file
m.
To see details on how the 32 bit addresses are translated
in the segmentation hardware in protected mode look here.